## Slide 1: Introduction to Broadband processing with Matlab
Rob Porritt
UC Berkeley PhD Candidate
IRIS Internship Orientation, Socorro, NM. May 2011

## Slide 2: Data comparison
Hunter
Pnina
Rob
Cork was a George Bush (failure)

## Slide 3: Some interesting signals
20 seconds ~ 160 km

## Slide 4: Disclaimer
I primarily work in c for the processing speed and my familiarity with it.
The Matlab functions in this tutorial were written by me, a graduate student in seismology, not a computer programmer or an expert in digital signal processing.

## Slide 5: Why Matlab?
Pros:
  Easy to use and learn
  interactive environment
  ever-growing library
  good documentation
Cons:
  Not free
  Slow to open
  Poor with strings

## Slide 6: Matlab packages available
Fissures-MATLAB
  Package distributed by IRIS
MatSeis
  Package for active source data processing
SplitLab
  Package for doing shear-wave splitting

## Slide 7: Get your own copy
You can copy the data and functions from my directory on a linux/unix terminal with the command:
    cp –r /fs/tmp/porritt_matlab/* .
Now you can call them from matlab or edit them with the editor.
Check out the functions
  ls porritt_broadband_processing_matlab/functions

## Slide 8: Get started
Download a local copy:
  http://seismowiki2.pbworks.com/f/porritt_broadband_processing_matlab.zip
Unzip
  Gunzip or finder
Add the path
  Launch matlab. Then:
    addpath (directory of unzipped)/porritt_broadband_processing_matlab/functions

## Slide 9: Add matTaup
Not sure we’ll get there, but to install the matlab wrapper from Matlab prompt:
  addpath /Users/usarray/Documents/MATLAB/matTaup/
  javaaddpath /Users/usarray/Documents/MATLAB/matTaup/lib/matTaup.jar

## Slide 10: Not just for data processing
Start with a break
  Matlab draw poker
    poker
  Matlab role-playing game
    dungeon
I made these games years ago during a very boring summer working third shift in an automotive factory.

## Slide 11: My favorite equations (1)
u(t) = s(t) * g(t) * i(t)
or
U(ω) = S(ω)G(ω)I(ω)
The observed seismogram (u) is a convolution of the source (s) of seismic excitation with the earth’s Green’s function (g) and the convolution with the instrument recording (i). Or in the frequency domain, convolution is multiplication.

## Slide 12: My favorite equations (2)
ρü = f + (λ + 2μ)∨(∨u) – μ∨ x (∨ x u)
The equation of motion in a homogeneous medium, using displacement variables:
Quantitative Seismology, Aki and Richards, 2002. Equation 4.1
Or as Sir Isaac Newton put it:
MA = ΣF

## Slide 13: Data
Some data from a Berkeley station is stored in the data/exercise_{1,2,3,5} folders
You can replace that data with your data in the folder data/chile_6.4/
Inside that folder are three more folders (porritt, miller, anthony) which contain data for a teleseism.
Inside data/ is the pole-zero response of your stations (cmg3t.pz)
Last year’s data is in data/intern_data if you’re interested

## Slide 14: Component naming convention
First letter is the sampling rate
  L = Low or 1 hz
  B = Mid or 40 hz
  More options, but these are most likely what you may see
Second letter is the gain
  H = High gain
  L = Low gain
Third letter is the direction
  Z = Vertical
  N = North
  E = East
  Thus, BHZ is 40 hz, high gain, vertical

## Slide 15: Preprocessing
From here on, the full steps are outlined in the worksheet.
The rest of the presentation will hopefully give background why we do each step, but feel free to start working
Preprocessing is the “standard” steps to get true ground motion from the seismic record
Raw data is in “digital counts” versus time.

## Slide 16: Preprocessing
Remove the mean and linear trend
  The mean would create a very large DC or 0 frequency amplitude.
  The linear trend has a lesser effect, but again amplifies various non-linear effects
Taper the ends
  The Discrete Fourier Transform (DFT) algorithm can create significant undesired sidelopes or ringing. Tapering the ends reduces this effect
Remove the instrument response
  This is a science in and about itself (see next slide)

## Slide 17: Instrument Response
Convolution of sensor, digitizer, and decimation(s).
Sensors has poles to define shape, zeros to define acceleration, velocity, or displacement, and gain for units.
Digitizer does decimation with gain factor and high corner poles
My function does not include digitizer poles and normalization because the sac pole zero file does not contain that information.
Frequency (Hz)
Amplitude

## Slide 18: Integration and Differentiation
We record velocity as a function of time, but moment tensors are defined in terms of displacement and building codes are defined in terms of peak ground accelerations
Thankfully the relations are standard calculus
Sadly they are discrete functions and thus its non-trivial to implement the calculus

## Slide 19: Integration and Differentiation
How to integrate or differentiate in the time domain is actually non-trivial. It is thus more common to do frequency domain calculus.
freq_integrate
  Divides the data by 2iπf
freq_differentiate
  Multiplies the data by 2iπf
Displacement
Velocity
Acceleration

## Slide 20: Long period seismograms
Many factors discussed in the worksheet lead to primarily long period signals from large distant earthquake
Large earthquakes excite very large and very long period waves which ring around the earth
The longest period earth mode is the Slichter mode vibrating with a period of around 1 hour.

## Slide 21: Exercise
Preprocess the 3-component data to ground velocity
Low pass filter the data
Rotate the horizontals to radial and transverse directions.
If you feel comfortable with Matlab try plotting phases with plot_phases described at the end of the worksheet.

## Slide 22: Anthropogenic noise
“Noise” due to human motion typically excites higher frequencies.
High pass filter the data to see the variation between day and night
broadband
High passed
6am - Berkeley

## Slide 23: Power Spectral Density
Spectral estimate of power over a time period
Robust estimates require averaging several spectrums within the time window.
Standard tool for looking at background seismic signals and quality control of stations.

## Slide 24: Coherence
Measure of similarity between two signals
Robust estimate via similar method as PSD

## Slide 25: Cross Correlation
Estimates delay time of similar signals

## Slide 26: Phase arrival estimate
Function still needs work. Main inputs include the distance between station and earthquake, 1D velocity model, depth, and origin time relative to the start of the seismogram.
True P?
True S?
Rayleigh?
Notes: <number>

## Slide 27: Generalized Ray Theory
Forward Modeling method. Exercise is not fully developed. Delve into this only if you are exceedingly curious and comfortable with Matlab
Computes the rays with some esoteric law you may have heard of…

## Slide 28: Rays computed in code
Snell’s Law!