## Slide 1
Analysis of Recorded and Simulated Far-Field Ground Motion
From the Source Physics Experiment
Arben Pitarka, Robert J. Mellors, Oleg Y. Vorobiev, Ezzedine Souheil,Arthur J. Rodgers,
William R. Walter, Tarabay Antoun, Anders Petersson, and Jeff Wagoner.
State-of Analysis Review Meeting, Las Vegas
August 22, 2013

## Slide 2: Overview
Objective: Improve understanding of the excitation and propagation of seismic waves, especially shear waves, from underground explosions.
Approach:
Simulate near-field ground motion from underground SPE3 explosion using a physics based source model coupled with far-field viscoelastic wave propagation
Compare with observed waveforms from Source Physics Experiment.
Analyze path effects (scattering, topography, and structural variations) at close distances (< 20 km)
Long-term Goal: Create a physics-based end-to-end model for monitoring that couples hydrodynamics to elastics and allows for both scenario prediction and detailed analysis of observed signals

## Slide 3
Emplaced in granite
SPE1: 100 kg TNT at 55 m
SPE2: 1000 kg TNT at 45 m
SPE3: 1000 kg TNT at 45 m
SPE Shots
Sensors
Array of near-field borehole and surface accelerometers
Instruments deployed along 5
radial lines out to 20 km
Mix of short-period and broadband
Infrasound
Topography Along L1

## Slide 4: Observed Far-Field Shear Wave Energy
Broad-Band
Significant shear wave energy on the tangential component
Causes:
- source effects
- wave propagation effects?
(structural heterogeneity, surface topography)
400m
800m

## Slide 5
FK Analysis Using Small Array Data
Small Array Yucca Flat Basin
Azimuth
Apparent Velocity
Recorded Motion

## Slide 6
S-waves are produced in the near-field and seem to be consistent with motion on joints
Efforts are underway to improve the quantitative agreement with the near field data and correlate the observed anisotropic behavior to the underlying physical mechanisms
faults & geologic layers
Constitutive behavior of the rock
Joint properties
Effect of saturation
after Vorobiev et al

## Slide 7
Near-Field and Far-Field Coupling
One-way coupling between nonlinear, inelastic near-field and linear, visco-elastic far-field regions using a padding mortar space in 3D.
Near-field: 3D Lagrangian hydrodynamics code with non-linear material response (GEODYN-L)
    Explosion loading
    Compressional and tensile failure, yielding, porosity, cavity formation
    source mortar embedded within finite difference model
  Far-field: 3D-FDM (WPP)
    Driven by interpolated time series from GEODYN model
    Signals propagated through complex 3D velocity model of geology to distances of 10’s of kms
    Coupling verified and validated.
WPP
3D finite-difference code Curvilinear grid for topography, mesh refinement, viscoelastic model .Designed for massively parallel systems
WPP
GEODYNL
mortar

## Slide 8: 3D Underground Structure Large Scale Constraints of the 3D Velocity Model
3D Model Based on
Geology
Surface mapping
Boreholes
Geophysical models
Lithology Vp(km/s) Vs(km/s)
Softer Granite 4.34 2.50 H=60m
Granite: 6.20 3.58 no gradient
Paleozoic: 5.60 3.24 small gradient
Tertiary: 4.20 2.42 small gradient
Quaternary: 3.00 1.50 no gradient
Top Quaternary 2.00 0.90 H=80m
Stochastic Small Scale Heterogeneity (l=1km,up 15%)
(Wagoner,2012)

## Slide 9
2.5D Modeling of Shallow Structure
in Granite
Coda Interferometry
(Matzel et al. 2013
Mellor’s talk)
Models of Surface Weathered Layer for L1 (Max Freq 10 Hz)
Vs
Vp
Vs

## Slide 10
Small Scale Shallow Variations
Stochastic Small Scale Heterogeneity (L=1km,up 15%, Gaussian weighting)

## Slide 11: Simulations reveal very complex propagation and clear conversions of P and Rg energy to S-wave energy
5 km
5 km
10 km
P
pS
Rg
S
P
pS
Rg

## Slide 12
3D Simulation Using Source Coupling
3D Model & Topography
(Max Freq:10Hz)
Line 1 Granite

## Slide 13
Line 3 Alluvium
The alluvium structure needs improvements

## Slide 14
L1-16
Granite
Basic 3D Velocity Model

## Slide 15
L1-16
Basic 3D Velocity Model
+ Surface Weathered Layer
Weathered layer increases amplitude and duration

## Slide 16
L1-16
Basic 3D Velocity Model
+ Surface Weathered Layer
+ Topography and Stochastic Heterogeneity
(L=1km,up 15%)
Topography and Stochastic Heterogeneity increases amplitude on the transverse component

## Slide 17
L3-12
Alluvium
Basic 3D Velocity Model
+ Surface Weathered Layer
+ Topography and Random Variations

## Slide 18



Receiver Located 4 km Below
the Source
Significant presence of scattering effects
local and regional ray paths

## Slide 19
T=50 ms
Free surface
Fixed boundary
3D Velocity contours
source
A6
A7
Sensitivity of Far-Field Motion To Source Modeling
(Effect of Gravity)

## Slide 20
L1
L3
Effects of Gravity

## Slide 21
P
Rg
P
Vertical
Sdirect
Transverse
Sscatter
Sscatter
Sdirect
Effects of Gravity Max Freq: 6Hz
200m
1600m

## Slide 22
Model 1
Model 2
Model 3
Sources With Different Equally Probable Joint Network
Using Site Fracture Characterization
Snapshots of particle velocity amplitude at 10ms, for different sources, computed with
3 different realizations of fracture networks embedded in Geodyn-L.

## Slide 23
Vertical
Transverse
Effects of Joints Orientation on the Far-Field
Radial
Max Freq: 6Hz

## Slide 24
Conclusions
Coupling of explosion 3D hydrodynamic simulation with anelastic wave propagation modeling improves the quality of simulated waveforms for the SPE
The combined effects of surface weathered layer, surface topography and small scale structural heterogeneities have a significant impact on creation and amplitude of shear motion during underground explosions
In addition to shear waves generated at the source, shear waves generated by near-surface structural complexities propagate at local distances. The increase in shear-wave energy could explain why the P/S discriminant for SPE explosions does not work well for some azimuths at local distances.
Stochastic realizations of joints based on site fracture characterization produce similar shear and compressive far-field ground motion in the modeled frequency range up to 6Hz.

## Slide 25: Acknowledgements
Thank you!