## Slide 1: Discrete and continuum simulations of near-field ground motion from SPE
Oleg Vorobiev , Souheil Ezzedine,
Eric Herbold, Tarabay Antoun and Lew Glenn
Lawrence Livermore National Laboratory
State of Analysis Review
August 21-22, 2013
Las Vegas

## Slide 2: What can we learn from near field modeling ?
Shear-wave generation, implications for monitoring
Role of site characterization
Role of surface and gravity
Scalability with yield
Source model for the far field
Notes: Horizontal shear motion cannot be produced in an Isotropic and orthotropic medium!
What is important in site characterization – faults, joints, layers, microcracks may be? How much data we could digest for analysis
When do we see spall signal?
Can we always rely on cube root scaling?
Assuming we know enough what would be our source model?

## Slide 3: Joints can redirect energy flow from the source
Sugar shot (Melzer, 1970)
Small charge
Sugar cubes
Small scale experiment
High confinement
Low confinement
Joint sets at SPE site
Random joints
Vorobiev, IJNME, 2010
Notes: We can expect joint effects on wave propagation based on our previous experience

## Slide 4: Parallel nonlinear code GEODYN-L is used to model near-source ground motion
Dimensions:
joint aperture ~1 mm
joints spacing ~ 1 m
source size ~1 m
region ~300 m
Computational model:
~20-50 million elements
~100-200 million zones
3240 CPU for 12 hours
N
Fault 2
Fault1
300 m
150 m
15 m
Notes: We have to resolve diverse time and space scales in calculations

## Slide 5
Discrete-continuum simulation of SPE3 using GEODYN-L
SPE3 discrete model: horizontal shear wave generation

## Slide 6: Vertical joint sets define polarity of horizontal shear motion
Horizontal shear motion of different polarity
p-wave
Sliding joints
Side view
Top view
Joint planes
Notes: We see correlation between joint orientation and polarity of shear waves

## Slide 7: 3D discrete model with 3 joint sets : sliding joints produce shear motion
#8-2
#9-5
N
t=2 ms
t=20 ms
R
R
T
T
data
calc
Notes: Magnitude of shear waves is comparable with experiment

## Slide 8: Two vertical joint sets used in calculations cannot explain observed shear motion
Data vs calculations at 20 m Range
T
R
#9-2 located at the source level
in normal direction to vertical joint set 1 (which corresponds to high dip angle sets Set-1 and Set-2)
calc
Rose diagram Map
9-2
Notes: Not all gauges are explained, but it turned out that the shear motion is quite sensitive to the joint orientation. Since not all joint orientations
Are present it may affect results at some locations. 9-2 is almost normal to set 1 but some joint directions are not modeled

## Slide 9: A single vertical joint generates shear motion but not over sufficiently wide azimuth
One joint, t=9 ms
2D: Motion at 10 and 20 m range for locations
oriented at various angles relative to the joint direction:
Joints slide if m > the friction angle
Not transmitted across the joint

## Slide 10: Increasing the number of joints widens the azimuthal region of shear motion
Velocity vectors and tangential velocity directions at 7 ms
Blue clock-wise, red counter-clock-wise.
Friction coefficient=0.6. Slip on the joints is shown in dark grey
Sliding joints
Increased joint density

## Slide 11: The azimuthal region with shear motion also widens with decreasing friction
Friction ~0.8
Friction ~0.4

## Slide 12: Anomalous high velocity can be explained by various joint properties in the vicinity of that gauge
Assumptions:
#7-2:
joint spacing= 2.5 m
Friction =0.4
Azimuth =30 degrees
#9-2:
Joint spacing = 1.6 m
Friction =0.2
Azimuth= 170 degrees
Time =6 ms
#9-2
#7-2
Data
Calculations

## Slide 13: Both discrete and continuum joint models assume that the joint spacing is bigger than the element size
DISCRETE JOINT
Contact element
Nonlinear normal compliance
Coulomb friction
Valid for large slips and separations
Isotropic material
Elastic-plastic
anisotropy
CONTINUUM JOINT
Weakness plane
No compliance
Coulomb friction
Small deformations
Isotropic material
plastic
anisotropy
Bigger domains, more runs
verify
We have employed a continuum joint modeling to study effects of joint orientations and gravity

## Slide 14: Discrete and continuum joint methods produce similar results where the flow is controlled by plasticity (2D)
Q=1 kJ/g
f=0.4
DISCRETE
CONTINUUM
Q=1 kJ/g
f=0.2
Q=0.4 kJ/g
f=0.2

## Slide 15: Discrete and continuum methods show similar results (3D)
Explosion in hard rock with three Cartesian
sets of
joints
Dependence on joint friction
Discrete joint representation
Friction=0.6
Friction=0.2
Continuum joint representation
Friction=0.6
Friction=0.2
Pressure contours (0-50 MPa)
Joint spacing 1 m, friction ~0.2
3
1
2

## Slide 16: Material tensile strength affects the vertical velocity calculated at the surface
T=50 ms
Free surface
Fixed boundary
3D Velocity contours
source
A6
A7
Calculation set up with gravity
G

## Slide 17: Continuum model with gravity provides reasonable agreement with the surface measurements in SPE3
Continuum joint model, 600mx600mx300m domain, 834 CPU, 6 hours

## Slide 18: We expect similar near field velocities in SPE4 as in SPE1 with less damage near the surface
Plastic Slip at the joints
R= 20 m
Calculated surface motion (SPE1 vs SPE4)
the model is calibrated for SPE3 data first

## Slide 19: Conclusions
Vertical Joints can cause significant horizontal motion comparable with that observed in the SPE experiments
Both joint spacing and friction angle affect the amount of produced shear motion.
The higher the friction, the shorter and more delayed is the pulse of the shear wave.
By controlling the joint friction and spacing in a reasonable interval one can describe shear waves that correlate with larger than expected P-wave motion.
Gravity is important to model the vertical velocity as well as the radial velocity near the surface
Effect of joint friction
Tangential motion cased by one set of joints

## Slide 20
For more information:
Oleg Vorobiev
vorobiev1@llnl.gov
925-423-5151
Auspices
This work was partially performed under the auspices of the U.S. Department of Energy by Lawrence Livermore National Laboratory under Contract DE-AC52-07NA27344.
Disclaimer
This document was prepared as an account of work sponsored by an agency of the United States government. Neither the United States government nor Lawrence Livermore National Security, LLC, nor any of their employees makes any warranty, expressed or implied, or assumes any legal liability or responsibility for the accuracy, completeness, or usefulness of any information, apparatus, product, or process disclosed, or represents that its use would not infringe privately owned rights. Reference herein to any specific commercial product, process, or service by trade name, trademark, manufacturer, or otherwise does not necessarily constitute or imply its endorsement, recommendation, or favoring by the United States government or Lawrence Livermore National Security, LLC. The views and opinions of authors expressed herein do not necessarily state or reflect those of the United States government or Lawrence Livermore National Security, LLC, and shall not be used for advertising or product endorsement purposes.

## Slide 21: 2D:Transverse and radial motion at 10 and 20 m ranges for 60-70 degree angles
The joints can explain not only
tangential motion but also wider radial displacements
due to energy redirection
(some azimuthal directions will have more and the other ones less energy)
Joint spacing ~2.5 m
Friction angle ~30 deg

## Slide 22: Increasing friction delays the shear motion and makes shear pulse shorter
A10
A45
A60
Friction effect
Location effect
Apparent delay
Friction angles=21,31,41
#7-2, R=20 m

## Slide 23: Gravity does not affect velocity histories at R < 20 m

## Slide 24: Generation of horizontal shear motion by vertical joints
T=1 ms
T=3 ms
T=7 ms
Sliding joints
Clock-wise shear
Friction coef.=0.4

## Slide 25: Pressure and velocity iso-surfaces for SPE4 explosion simulation (cross-section)
T=10 ms
T=50 ms
T=70 ms
Lithostatic pressure
Spherical wave
Reflected wave

## Slide 26
Polished joint in Limestone loaded by a shock wave
Vorobiev, O.Yu.,(2010),”Discrete and continuum methods for numerical simulations of non-linear wave propagation in discontinuous media”, International Journal for Numerical Methods in Engineering,83,482-507
Joint model has been validated for dynamic conditions

## Slide 27: Joint model has been validated for quasi-static conditions
Shear test simulation
Joint softening effect
Nonlinear dilatancy